## Slide 1: Wind Turbine Fault Prediction and Maintenance Scheduling: The Use of Machine Learning Techniques
Author: Hanchao Chen
Supervisor: Matthew Piggott
Co-supervisor: James Percival
8th September, 2020

## Slide 2: Contents
Background
Data Overview & Pre-processing
Regression Model
Binary Classiﬁcation Model
Multinomial Classiﬁcation Model
Conclusion and Future Work
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 3: Background
Wind energy: clean, free, renewable
Offshore wind farm
Difficulties:
high failure rate, the long downtime, and the low reliability
Operation and Maintenance (O&M):
25~30% production cost
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 4: How to reduce O&M cost
Accurate reliability assessment and fault prediction of wind turbines.
Remind the operators of necessary maintenance and repair of the power converter before a serious fault.
Supervisory Control and Data Acquisition (SCADA)
Record the evolution of different parameters of wind turbines.
Data-mining
Machine learning
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 5: Main Contributions
Three different machine learning based models for assessing wind turbines’ health status
New pre-processing method
A standard workﬂow
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 6: Data Overview
Parameters record
Status record
instanceID | ts_start | ts_end | duration | status | code | message | comment | contractCategory | 
BEI_WTG07 | 2019/1/2 12:32 | 2019/1/2 12:44 | 0:12:20 | stop | 94 | Stopped untwisting cables |  | Cable Unwind | 
BEI_WTG07 | 2019/1/8 7:02 | 2019/1/8 8:53 | 1:51:03 | stop | 16 | Control voltage drop |  | Unscheduled Maintenance - Electrical System | 
BEI_WTG07 | 2019/1/8 7:05 | 2019/1/8 8:54 | 1:48:39 | warning | 50001 | No communication |  | <undefined> | 
BEI_WTG07 | 2019/1/8 8:56 | 2019/1/8 9:17 | 0:20:41 | stop | 51 | Low lower voltage exceeded | Turbine surrendered by Duncan Mcneil AWP 008, 08/01 further investigation required. | Unscheduled Maintenance - Electrical System | 
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 7: Data Pre-processing
Visualization & Variables selection
Density plot (diagonal)
Correlation plot (other)

## Slide 8: Data Pre-processing
Useless value removal
Missing values
Low output power values
Curtailment values
outliers
W. Soﬁa. Condition-Based Maintenance of Oﬀshore Wind Farms: The Use of SCADA Data in Normal Behavior Modelling. Master’s thesis, Imperial College London, 2018.
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 9: Regression Model
ANN vs. LSTM

## Slide 10: Regression Model
Abnormal evolution
Prediction vs. Real
deviation
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 11: Binary Classification Model
Numerical Label
0 normal state
1 failure state
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020
1.0
0
Label
evolution
Normal state
Failure state
Early state of failure

## Slide 12: Binary Classification Model
Test on LLY-21
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 13: Multinomial Classiﬁcation Model
New data pre-processing strategy
Active variables:
Passive variables:
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020
ambient temperature, power, wind speed
gear oil temperature, generator RPM,
generator temperature,
high speed bearing temperature…
2D view
3D view

## Slide 14: Multinomial Classiﬁcation Model
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020
Operating state (clusters)
Active variables
Passive variables
Single data point
decide
predict
High accuracy
Low accuracy
Normal
Failure
Belong to

## Slide 15: Multinomial Classiﬁcation Model
Test on LLY-21
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020

## Slide 16: Conclusion
Three machine learning based models, three aspects.
A new pre-processing method (cluster method)
A standard workﬂow
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020
“off line” training, “on line” prediction
Efficient, great potential
Future Work
Combine LSTM with Multinomial Classiﬁcation Model
Revise the cluster method
Methods of processing time series

## Slide 17: THANKS
Wind Turbine Fault Prediction and Maintenance Scheduling
8th September, 2020